## Slide 1: Milestone 1
Team 2 (Zhenbo Gao, Baran Kiliç, Ben Garbe)
13.05.2026

## Slide 2
Overview
Tasks | Status | Notes
Explore hardware modules | Done | 
3D print sensor mounts | In progress | Camera mount printed Lidar mount designed
Robot movement | Done in simulation | Robot can move from one point to another with Nav2
Setup ROS2/ ROS2 Gazebo | Done | Integrated a simulated lidar to map the area
SLAM-algorithm simulation/real world | Done (real world) | slam_toolbox mapping Map saved (pgm/yaml + posegraph/data) Localization mode /robot_pose topic

## Slide 3
Zhenbo Gao
  SLAM & Localization: Real-time mapping with slam_toolbox; publishes /map, /robot_pose
  Perception & Object Detection: Color recognition (HSV) + 3D block pose via RealSense depth camera
Baran Kiliç
  Ros2 / Gazebo Simulation
Ben Garbe
  Hardware
  Robot Arm Control
Tasks & Responsibilities

## Slide 4
Hardware Tasks
First Version of Kamera mount designed and printed
Lidar tower mount designed
Sensor Mounts

## Slide 5
Hardware Tasks
Started with design for 2 DoF Robot Arm
Robot Arm

## Slide 6
Ros2 and Gazebo Tasks
RVIZ with robot with a simulated lidar sensor
RVIZ and Gazebo

## Slide 7
Ros2 and Gazebo Tasks
Nav2 navigation showcase
Nav2 navigation

## Slide 8
SLAM Tasks
SLAM: Mapping & Localization
Mapped the arena using slam_toolbox
LIDAR scan fused with wheel odometry
Map size: 2.25 m × 2.35 m, covering the 2 m × 2 m arena
Saved in pgm/yaml + posegraph/data format
Slow speed
Medium speed
Localization mode: robot loads pre-built map and estimates its position in real time using LIDAR
/robot_pose topic: outputs current position (x, y, heading) at 10 Hz → consumed by Nav2